## Slide 1
5. Disaster types, risk assessment and safety measures
Study course "Civil Protection"
Developed in the framework of the European Commission’s Civil Protection Financial Instrument "Track1" project "Establishment of comprehensive civil protection and disaster management training for governmental institutions, civil protection commissions of municipalities, universities, Fire Safety and Civil Protection College, as well as establishing safety advice for the public" (ECHO/SUB/2022/TRACK1/884396)​
Funded by The European Union
State Fire and Rescue Service

## Slide 2: Tasks
Educatees:
      know the different types of disasters and how they are classified;
      know the basic principles and action steps of disaster management;
      can describe the main principles of safety measures.
Intended results
To introduce educatees to:
types of disasters;
key principles of disaster management, including prevention, preparedness, response and recovery;
the principles of disaster risk assessment;
key principles for safety measures.

## Slide 3: Table of contents
5.1. Categorisation of disasters
5.2. Principles of disaster management
5.3. Disaster risk assessment
5.4. Safety measures
5.4.1. Hazardous substances
5.4.2. Personal protective equipment

## Slide 4: Introductory discussion with educatees on the categorisation of disasters
How can disasters be categorised? Why is it important to do this?
Do you know how prevention, preparedness, response and recovery measures differ? Have you ever been involved in any of these?

## Slide 5: 5.1. Categorisation of disasters

## Slide 6: Definition of a disaster
Has caused human casualties or endangers human life or health
Caused damage or threat to people, the environment or property
Inflicted or inflicts significant material and financial losses
Exceeds the daily capacity of the responsible State and local government authorities to prevent the devastating conditions
An accident which:
Civil Protection and Disaster Management Law
5.1
5.2
Categorisation of disasters
5.3
5.4

## Slide 7: Categorisation of disasters according to cause Natural disasters
Natural disasters
Geophysical
Hydrological
Meteorological
Climatological
Biological
Cosmic*
Earthquakes
Landslides
Heavy rainfall, hail
Snow drifts
Storms, whirlwinds
Epidemics
Epizootics
Epiphytoties
Floods
Icing
Drought
Fires in forests and peat bogs
Heat
Intense cold, snow
*The State civil protection plan does not include cosmic disasters
Civil Protection and Disaster Management Law
5.1
5.2
Categorisation of disasters
5.3
5.4

## Slide 8: Categorisation of disasters according to cause Anthropogenic or man-made disasters
Anthropogenic or man-made disasters
Technogenic disasters
Release of substances
Fires in buildings and structures
Collapse of buildings and structures
Ruptures in dams and other hydrotechnic structures
Damage to electricity networks
Accidents in utility networks
Public disorder,
Internal conflict
Terrorist attacks
Chemicals
Biological substances
Radiation
Vehicle accidents
Aviation
Road transport
Railway
Ships
Civil Protection and Disaster Management Law
5.1
5.2
Categorisation of disasters
5.3
5.4

## Slide 9: Disasters by scale of damage caused
Regional disasters- the scale of damage caused by a disaster exceeds the borders of the administrative territory of one local government
State disasters - the scale of damage caused by a disaster affects the entire territory of the State or a significant part thereof
What examples can you give of disasters of different scales?
Local disasters - the scale of damage caused by a disaster does not exceed the borders of the administrative territory of one local government
Civil Protection and Disaster Management Law
5.1
5.2
Categorisation of disasters
5.3
5.4

## Slide 10: 5.2. Principles of disaster management

## Slide 11: A set of disaster management measures taken to ensure that civil protection tasks are carried out
Preparedness measures
Preventive measures
Measures for the elimination of consequences
Response
measures
Recovery
measures
Disaster
Management
EVENT
Disaster management - a set of managed and coordinated preventive, preparedness, response, elimination of consequences measures, and also recovery measures conducted to ensure the implementation of civil protection tasks.
Disaster management is coordinated by:
Ministry of Defence
Ministry of Foreign Affairs
Ministry for Climate and Energy
Ministry of the Interior
Ministry of Environmental Protection and Regional Development
Ministry of Transport
Ministry of Health
Ministry of Agriculture
local governments
5.2
5.3
Principles of disaster management
5.4
5.1

## Slide 12: Preventive measures
Examples:
The SFRS organises public education activities to raise awareness of safety issues, to reduce the number of people killed and injured in fires and other accidents, and to inform the public about the principles of fire safety, firefighting, rescue and civil protection.
Preventive measures - a set of measures performed to prevent or reduce the threats of a disaster.
Public education
Ice blasting to prevent flooding
Ice blast in Ogre
5.2
5.3
Principles of disaster management
5.4
5.1

## Slide 13: Preparedness measures
Examples:
State Material Reserves (SMR)
National early warning system
A national early warning system is a stand-alone technological system or set of such systems that provides early warning - notification of a disaster or disaster threat and the necessary action.
The system includes alarm sirens, public media (radio, TV, LTV and LR), alarm and notification equipment for state and local authorities, emergency transport and other solutions.
Preparedness measures - a set of measures performed to prepare for the required action in case of a disaster.
5.2
5.3
Principles of disaster management
5.4
5.1
SMR are a pool of material and financial resources established in accordance with the law and used by institutions involved in disaster management when the resources at their disposal are insufficient to carry out response activities.
SMR are used in disaster management response, recovery and reconstruction, crisis management, military threat management, humanitarian assistance, etc.

## Slide 14: Response measures
Information is distributed:
In the electronic media
On SFRS social media accounts and the 112 app
With the help of alarm sirens
Examples:
Response measures - a set of the measures which are performed in order to reduce or eliminate devastating conditions and the consequences caused thereby, to prevent or reduce harm to people, the environment and property.
Activation of the National early warning system
Evacuation of the population
72 hours. Evacuation and resistance
5.2
5.3
Principles of disaster management
5.4
5.1

## Slide 15: Measures for the elimination of consequences
Restoring public services in evacuated areas
Assessing and restoring damage to the environment and infrastructure
In the event of flooding, relief measures include pumping water out of people's homes, sawing up and removing trees that have been cut down by water.
Measures for the elimination of consequences - a set of measures which are performed in order to ensure at least the minimum basic needs of inhabitants related to the survival of people and to stop or reduce threat to human health, the environment and property.
5.2
5.3
Principles of disaster management
5.4
5.1
Restoration of health, education, transport, water, electricity, communications and other essential services in evacuated areas, ensuring the basic needs and well-being of the community.
Examples:

## Slide 16: Recovery measures
Renewal of infrastructure
Compensation for damages
Recovery measures - a set of measures which are performed in order to help victims in a timely and proportional manner and to the extent possible to restore the environment and property to the state it was before the disaster.
5.2
5.3
Principles of disaster management
5.4
5.1
The Cabinet of Ministers shall determine the procedure for compensating a legal or natural person for expenses and losses incurred when its resources are involved in response and recovery operations, as well as the procedure for calculating the amount of compensation.
Examples:

## Slide 17: 5.3. Disaster risk assessment

## Slide 18: Key steps of disaster risk assessment
Disaster risk assessment recommendations
Risk identification is the process of identifying, recognising and describing risk.
Risk analysis is the process of understanding the nature of risk and determining its level.
Risk assessment is the process of comparing the results of a risk analysis against risk criteria to determine whether the risk and its level are acceptable or satisfactory.
Quantitative method (mathematical)
Qualitative method (based on events, expert opinion)
Semi-quantitative method (quantifies the probability of an accident and the consequences of the hazard)
Natural hazards
Technological hazards
Social hazards
Risk assessment is divided into 3 main steps:
1
Planning
2
The main event
3
Scenario
4
Impact on basic needs
5
Consequences
6
Vulnerability and capability
5.3
5.4
Disaster risk assessment
5.2
5.1

## Slide 19: Elements of a risk scenario analysis
Disaster risk assessment recommendations
The risk scenario analysis requires analysing the six elements in the following order.
The figure below summarises the content of the elements and the steps involved:
Element 1
Element 2
Element 3
Element 4
Element 5
Element 6
PLANNING
THE MAIN EVENT
SCENARIO
IMPACT ON BASIC NEEDS
CONSEQUENCES
VULNERABILITY AND CAPACITY
6.1. Assess whether it is possible to achieve the objectives while preserving the conservation values and functions
6.2. Assess prevention capacity
6.3. Assess vulnerabilities
6.4. Rate your ability to respond
6.5. Assess what vulnerabilities need to be reduced and what capacities need to be developed
5.1. Assess the implications for public safety values
5.2. Carry out a sensitivity analysis
5.3. Carry out uncertainty analysis
4.1. Identify what key societal needs are involved in responding to the scenario
4.2. Identify how this affects the maintenance of essential public services
3.1. Identify the "Worst credible scenario"
3.2. Set the start and end time
3.3. Select variables and variable values
3.4. Summarise the scenario
2.1. Identify the main event
2.2. Identify the factors that may lead to the occurrence of the event
2.3. Discuss the likelihood of a global event
2.4. Determine the capacity to prevent and respond to a global event
1.1. Organise the first meeting
1.2. Identify the need for information collection
1.3. Assess the need for consultation
1.4. Explore the need for external involvement
1.5. Set up a reporting plan
5.3
5.4
Disaster risk assessment
5.2
5.1

## Slide 20: Risk assessment matrix
Latvian risk matrix
Probability |  | Minor risk | Significant risk | Medium Risk | High risk | Very high risk
Very high | 1x per year and more often |  |  |  |  | 
Growing | 1x 1 - 15 years |  |  |  |  | 
Medium | 1x 16 - 50 years |  |  |  |  | 
Low | 1x 51 - 100 years |  |  |  |  | 
Very low | Less frequently than 1 x 100 years |  |  |  |  | 
 | Injured/victims | 10 to 100 | 101 to 1000 | 1001 to 5000 | 5001 to 10000 | more than 10000
 | Deaths | 1 to 10 | 11 to 100 | 101 to 500 | 501 to 1000 | more than 1000
 | Material damage | 50 000 to 100 000 | 100 000 to 1 million | 1 million to 10 million | 10 million to 100 million | more than 100 million
 | Environmental damage | 50 000 to 100 000 | 100 000 to 1 million | 1 million to 10 million | 10 million to 100 million | more than 100 million
 | The sick | Less than 5% | 5-15% | 15-20% | 21-35% | More than 35%
 | Displaced persons | 10 to 100 | 101 to 1000 | 1001 to 5000 | 5001 to 10000 | More than 10000
 | Consequences | Minor | Significant | Medium | Severe | Catastrophic consequences
Disaster risk assessment recommendations
On the National Civil Protection Plan
5.3
5.4
Disaster risk assessment
5.2
5.1

## Slide 21: Disaster risk summary State civil protection plan
Probability / confidence level | Minor risk | Significant risk | Medium risk | High risk | Very high risk
Very high |  | Forest and peat bog fires | Epizootics |  | 
High |  |  | Spring floods and high waters Heat Icing Public disorder Internal unrest | Epidemic, pandemic | 
Medium | Vehicle accident | Damage to energy networks Rail transport disaster | Strong frost Torrential and prolonged rainfall Thunderstorms and hail Whirlwinds Drought Snow and blizzards | Wind floods Damage to electricity distribution networks Storms and strong wind gusts Fires in buildings and structures | 
Low |  | Epiphytoties | Collapse of structures Breakdown in the natural gas supply system Passenger ship disaster On-site release of hazardous chemicals Wet snow deposit |  | Hydraulic structure breaks - Daugava HPP Spills of hazardous chemicals from ships
Very low | Landslides Earthquakes | Terrorist attacks Radiation accident Grounding of ships | Accidents in the oil product pipeline transport infrastructure Accidents or casualties in port and offshore hydraulic structures Vessel collision | Biological substance accident Aircraft accident | 
Potential level of consequence | Minor consequences | Significant consequences | Medium consequences | Severe consequences | Catastrophic consequences
Disaster risk assessment recommendations
On the State civil protection plan
5.3
5.4
Disaster risk assessment
5.2
5.1

## Slide 22: Example of risk assessment Risk analysis for floods and ice jams
For flood and ice jam risk, the primary indicator for the analysis was the sum of annual precipitation in the form of snow (GSS), for the period 1950 to 2100
The dark green line shows the GSS time plot calculated from the LVGMC observations
Snow cover is expected to decrease in the future, and peak floods are expected to decrease accordingly
Climate change will reduce both the likelihood and consequences of flood risks
 | Probability | Minor risk | Significant risk | Medium risk | High risk | Very high risk
Very high | 1x per year and more often |  |  |  |  | 
High | 1x 1 - 15 years |  |  |  |  | 
Medium | 1x 16 - 50 years |  |  |  |  | 
Low | 1x 51 - 100 years |  |  |  |  | 
Very low | Less frequently than 1 x 100 years |  |  |  |  | 
 |  | Minor | Significant | Medium | Severe | Catastrophic consequences
Daugavpils. Annual
The year
Annual snow amount
13%
87%
Median
Observations
5.3
5.4
Disaster risk assessment
5.2
5.1

## Slide 23: Example of risk assessment Risk assessment for floods and ice jams
The risk assessment considers:
  Socio-economic assessment of losses and benefits, identifying current and potential future losses
  Social vulnerability, identifying people at risk both by geographical location and social factors
Risks | Risk level | Affected group size | System adaptability | Assessment of economic losses | Vulnerability level
Spring floods and ice jams | 6 (risk with significant consequences and medium probability) | 5 (very large) | 3.75 (high) | 3 (medium) | 2.5 (medium)
  Assessment of the adaptive capacity of the system, with experts assessing different criteria of adaptive capacity for a given risk
  Vulnerability assessment, taking into account the results of all the categories analysed above
5.3
5.4
Disaster risk assessment
5.2
5.1

## Slide 24: Example of risk assessment Identified adaptation measures
No. | Adaptation measures | Prevention | Emergency planning and management | Post-disaster assistance and insurance
1 | Establishing a single disaster damage database |  | x | x
2 | Early warning |  | x | 
3 | Improving the monitoring and forecasting system | x | x | 
4 | Adaptation of the spatial plan and relevant legislation | x |  | 
5 | Education (a safety course is planned) | x | x | 
Taking into account various risk analyses, including flood and ice jam risk assessments, climate change adaptation measures have been set in the area of civil protection and emergency aid.
5.3
5.4
Disaster risk assessment
5.2
5.1

## Slide 25: 5.4. Safety measures

## Slide 26: Hazardous substances Definition and types
Hazardous substances are generally chemicals or metals that, because of their physical properties, pose an immediate hazard and can cause dangerous injury or death for a variety of reasons. Some can cause injury just by coming into contact, while others can cause harm by reacting chemically with other substances.
Types of hazardous substances:
Substances with a direct traumatic effects, which may cause harm with or without a pre-existing chemical reaction.
Oxidising agents, which generate oxygen, either naturally or by heating, increasing the risk of fire or explosion.
Water-sensitive materials that react with water or steam to produce heat or flammable explosive gases.
Toxic substances that poison the system through inhalation, ingestion or absorption through the skin.
Some substances can be classified in more than one of these categories and therefore pose an even greater risk.
5.4
Safety measures
5.3
5.2
5.1

## Slide 27: Hazardous substances Hazard symbols (1/5)
Hazard symbols for chemicals according to Regulation (EC) No 1272/2008 of the European Parliament and of the Council
O: Oxidising
E: Explosive
Xn: Harmful
Xi: Irritant
T: Toxic
T+: Very toxic
N: Dangerous for the environment
F: Flammable
F+: Extremely flammable
C: Corrosive
5.4
Safety measures
5.3
5.2
5.1

## Slide 28: Hazardous substances Hazard symbols (2/5)
GHS (Globally Harmonised System) pictograms and hazard classes
Unstable explosives, self reactive substances and mixtures, organic peroxides
Gases under pressure and dissolved gasses
Acute toxicity (oral, dermal, inhalation)
Flammable, self-reactive or self-heating substances and mixtures, pyrophoric liquids etc.
Corosives, serious eye damage
Acute toxicity, skin, eye irritation, skin sensitisation, organ toxicity, respiratory tract irritation, narcotic effects
Oxidising gases, liquids, solids
Acute toxicity (oral, dermal, inhalation)
Hazardous to the aquatic environment
5.4
Safety measures
5.3
5.2
5.1

## Slide 29: Hazardous substances Hazard symbols (3/5)
ADR transport pictograms and hazard class (1/3)
Explosive, subclass 1.1
Mass explosion hazard
Explosive, subclass 1.4
No significant hazard
Explosive, subclass 1.6
Extremely insensitive articles with no mass explosion hazard
Explosive, subclass 1.2
Projection hazards
Explosive, subclass 1.5
Very insensitive substances with mass explosion hazard
Explosive, subclass 1.3
Fire hazard or minor projection hazard
Flammable gas
5.4
Safety measures
5.3
5.2
5.1

## Slide 30: Hazardous substances Hazard symbols (4/5)
ADR transport pictograms and hazard class (2/3)
Flammable gas
Flammable liquids
Substances which, in contact with water, emit flammable gases
Non-flammable, non-toxic gases
Flammable solids, self-reactive substances and solid desensitized explosives
Oxidising substances
Toxic gases
Substances liable to to spontaneous combustion
Organic peroxides
5.4
Safety measures
5.3
5.2
5.1

## Slide 31: Hazardous substances Hazard symbols (5/5)
ADR transport pictograms and hazard class (3/3)
Toxic substances
Radioactive materials
Category I
Criticality safety index label
Poison
Radioactive materials
Category II
Corrosive substance
Infectious substances
Radioactive materials
Category III
Miscellaneous dangerous substances and articles
5.4
Safety measures
5.3
5.2
5.1

## Slide 32: Hazardous substances Storage of hazardous substances
A reservoir is a structure (e.g. tank, cylinder, basin) for storing a substance (usually liquid or gaseous)
The reservoir consists of:
Regulation on requirements for the design, installation, conformity assessment and market surveillance of storage tanks for dangerous chemicals and chemical preparations (products)
Level 2 containment - protective systems that prevent the release of a stored flowable substance into soil or groundwater if a leak or seepage occurs in a container or equipment. The containment system shall include double walls, synthetic membrane strips, prepared earth bunds, concrete barriers or equivalent materials to prevent the release of spillages
Technological equipment for the safe and suitable storage of substances, as well as elements attached to the container surfaces (e.g. hatches, joints, supports, handles)
Permanently installed tanks
5.4
Safety measures
5.3
5.2
5.1

## Slide 33: Hazardous substances Requirements for storage tanks for hazardous substances
Display clearly visible pictograms and warning signs on the reservoir to ensure correct use!
According to the type of tank, the following shall be indicated the following additional information
The following information shall be displayed on each tank:
the address, name or business name of the manufacturer or contractor
year of construction or manufacture and installation of the tank
other information deemed necessary by the manufacturer
identification data of the tank according to its type (e.g. tank type, series, number)
the main maximum and minimum limit values, operating temperature and storage volume
the identification number of the notified body which has carried out the conformity assessment of the storage tank concerned
reservoir volume
test pressure and test date
adjusted pressure of safety devices
maximum filling level or height
labelling of stored dangerous chemicals or chemical preparations (products) in accordance with the regulatory enactments on the procedure for classification, labelling and packaging of chemicals and chemical preparations (products)
5.4
Safety measures
5.3
5.2
5.1

## Slide 34: Hazardous substances Requirements for storage and use of dangerous substances and mixtures
Occupational health and safety requirements for working with chemicals and mixtures
Hazardous substances shall be stored separately in strictly defined areas equipped with local exhaust ventilation
Spilled or spilled substances shall be collected immediately - solids shall be swept up, liquids shall be collected with suitable absorbent material (granules, sand, cloth, etc.) and disposed of safely
Prohibited adjacent storage of flammable substances and oxidising substances
Liquid acids shall not be stored above eye level and shall be placed on lower shelves
They shall be stored on shelves according to their hazard classes and compatibilities
5.4
Safety measures
5.3
5.2
5.1

## Slide 35: Hazardous substances Dangerous Goods Identification and Code of Conduct Plaques
Dangerous goods identification plate
Emergency Action Code
Emergency Action Code Card in case of fire or leak Coarse spray. Fine spray. Foam. Dry absorbent. |  |  |  | Further information: Dry absorbent - water must not come into contact with the substance or mixture. V - In case of ignition, the substance may react rapidly and cause an explosion. LTS - Light chemical protective suit with compressed air breathing apparatus (BA). Dilute - can be washed off with plenty of water. Contain - Do not allow the substance to enter drains or water bodies. E - Warn people to stay indoors in confined spaces with the possibility of evacuation.
P | V | LTS | DILUTE | 
R |  |  |  | 
S | V | BA& FIRE KIT |  | 
T |  |  |  | 
W | V | LTS | CONTAIN | 
X |  |  |  | 
Y | V | BA& FIRE KIT |  | 
Z |  |  |  | 
E Public Safety Hazard |  |  |  | 
Hazard identification number (Kemler code)
UN number of the substance
Emergency designation
5.4
Safety measures
5.3
5.2
5.1

## Slide 36: Hazardous substances Safety Data Sheets
Safety Data Sheets (SDS) are a key tool to ensure that manufacturers and importers communicate sufficient information along the supply chain to allow substances and mixtures to be used (stored and disposed of) safely.
The SDS does not have to be supplied to the general public
The content of the SDS is the responsibility of any supplier
Supplier verifies adequacy of the SDS or updates it (by communicating it to the manufacturer)
The SDS must be kept for at least 10 years
Renewed and issued free of charge for all deliveries in the past 12 months
Provided on the first delivery no later than the same day
SDS issued in the Republic of Latvia must be in Latvian (Article 31(5) REACH)
The SDS must be drawn up in accordance with Annex II of REACH
SDS can also be issued electronically
Guidelines for the preparation of Safety Data Sheets
5.4
Safety measures
5.3
5.2
5.1

## Slide 37: Personal protective equipment Legislative framework
PPE is divided into:
Personal protective equipment (PPE) is articles, devices, equipment and systems worn or otherwise used at work by an employee to protect their safety and health from exposure to one or more risk factors in the working environment.
Head protective equipment
Hearing protective equipment
Face and eye protective equipment
Respiratory tract protective equipment
Hand and arm protective equipment
Trunk and abdoment protective equipment
Fall protective equipment
Skin protective equipment
Protective clothing against exposure to harmful factors at work
Foot and leg protective equipment
Labour Protection Requirements When Using Personal Protective Equipment
Read the occupational health and safety requirements carefully!
5.4
Safety measures
5.3
5.2
5.1

## Slide 38: Personal protective equipment Composition of personal protective equipment for workers in the health sector
Pants
[Image]
Gloves
[Image]
Coveralls
[Image]
Boots
[Image]
Safety goggles
[Image]
Caps
[Image]
Jacket / shirt
[Image]
Face protection
[Image]
National Disaster Medicine Plan 2020
5.4
Safety measures
5.3
5.2
5.1

## Slide 39: Sources of information (1/2)
Images sourced from the website "Unsplash". https://unsplash.com
Civilās aizsardzības un katastrofas pārvaldīšanas likums. https://likumi.lv/ta/id/282333
Eiropas Komisija. Bīstamas vielas. https://ec.europa.eu/taxation_customs/dds2/SAMANCTA/LV/Safety/DangerousSubstances_LV.htm
European Chemicals Agency. Vadlīnijas par drošības datu lapu sagatavošanu. https://echa.europa.eu/documents/10162/23036412/sds_lv.pdf/0e0c8ba2-63d9-4c95-9187-9de6a50fcac6
LTV Ziņu dienests. 72. stundas. Evakuācija un pretošanās. https://www.youtube.com/watch?v=EqTN-akzLIc
LTV Ziņu dienests. Ogrē spridzina ledu. https://www.youtube.com/watch?v=7fol0QqgihA
LV portāls. 2020. Kas ir valsts agrīnās brīdināšanas sistēma. https://lvportals.lv/skaidrojumi/320034-kas-ir-valsts-agrinas-bridinasanas-sistema-2020
Ministru kabineta 2002. gada 20. augusta noteikumi Nr. 372 "Darba aizsardzības prasības, lietojot individuālos aizsardzības līdzekļus". https://likumi.lv/ta/id/65619
Ministru kabineta 2006. gada 25. aprīļa noteikumi Nr. 339 "Noteikumi par prasībām bīstamo ķīmisko vielu un ķīmisko preparātu (produktu) uzglabāšanas rezervuāru projektēšanai, uzstādīšanai, par to atbilstības novērtēšanas kārtību un tirgus uzraudzību". https://likumi.lv/ta/id/134571
Ministru kabineta 2017. gada 7. novembra noteikumi Nr. 658 "Noteikumi par civilās aizsardzības plānu struktūru un tajos iekļaujamo informāciju". https://likumi.lv/ta/id/294938
Ministru kabineta 2017. gada 8. augusta noteikumi Nr. 440 "Valsts agrīnās brīdināšanas sistēmas izveidošanas, darbības un finansēšanas kārtība". https://likumi.lv/ta/id/292740
Ministru kabineta 2019. gada 18. jūnija noteikumi Nr. 268 "Valsts materiālo rezervju izmantošanas un pārbaudes kārtība". https://likumi.lv/ta/id/307788
Ministru kabineta 2020. gada 26. augusta rīkojums Nr. 476 "Par Valsts civilās aizsardzības plānu". https://likumi.lv/ta/id/317006
Ozola, A. Drošības datu lapas. Paplašinātās drošības datu lapas – DDL + Iedarbības scenāriji. https://www.meteo.lv/fs/CKFinderJava/userfiles/files/4_DDL+Iedarbibas%20scenariji(2).pdf
Procesu analīzes un izpētes centrs. 2017. Risku un ievainojamības novērtējums un pielāgošanās pasākumu identificēšana civilās aizsardzības un ārkārtas palīdzības jomā. https://www.varam.gov.lv/sites/varam/files/data_content/civila_aizs_arkartas_palidziba.pdf
Rīgas Stradiņa universitāte, Darba drošības un vides veselības insitūts. 2017. Darba aizsardzības prasības darbā ar ķimiskām vielām un maisījumiem. http://stradavesels.lv/Uploads/2018/03/20/329_2017_Atgadne_stradajot_ar_kimiskam_vielam.pdf
Tēzaurs: rezervuārs. https://tezaurs.lv/rezervu%C4%81rs:1
Valsts materiālo rezervju likums. https://likumi.lv/ta/id/302995

## Slide 40: Sources of information (2/2)
Valsts ugunsdzēsības un glābšanas dienests. Katastrofu riska novērtēšanas rekomendācijas. https://www.vugd.gov.lv/lv/media/340/download
Veselības ministrija. 2020. Valsts katastrofu medicīnas plāns 2020: Ieteikumi individuālo aizsardzības līdzekļu lietošanai veselības nozarē strādājošajiem. https://www.nmpd.gov.lv/lv/media/592/download